;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;
; This example illustrates how to generate a PWM asymmetrically. The duty cycle
; is to be updated by the host application by writing the new duty cycle (compare value) to
; the MOV32 data field. When there is a compare match, the MOV32 instruction will move
; the new compare value to the ECMP instruction. The update of the ECMP is considered
; synchronous as the update is only done with respect to the LRP (loop resolution period)
; time base and only when there is a compare match.
;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;

PWM_PERIOD .equ 1
PWM_PIN_NUM .equ 2
INIT_COMPARE .equ 3
INIT_HR_DELAY .equ 5

; Use CNT to generate a virtual counter. The counter period is changable by the host
; application. When counter reaches the PWM_PERIOD value, a DMA request is generated. The
; HTU is setup to take this request and return a new duty cycle. The new duty cycle will
; be written to the MOV32 data field as the new compare value.

L00 CNT { reqnum=0,request=GENREQ,reg=A,irq=OFF,max=PWM_PERIOD};

; ECMP is setup in high resolution mode to create a compare value against the current
; counter value in CNT instruction. Whenever, there is a match, it will set the specified
; pin low until the end of the PWM period. The pin starts as high at the beginning of the
; PWM cycle. The specified pin is changable by the host application.

L01 ECMP { next=L03,hr_lr=HIGH,en_pin_action=ON,cond_addr=L02,pin=PWM_PIN_NUM,
        action=PULSELO,reg=A,irq=OFF,data=INIT_COMPARE,hr_data=INIT_HR_DELAY};

; MOV32 instruction is only executed when ECMP has a compare match. When this instruction
; is executed, it will copy its data field value which contains the latest duty cycle (
; the compare value) back to ECMP's data field. The MOV32's data field is updated by the HTU
; with the new duty cycle value when responding to the request by the CNT instruction.

L02 MOV32 { remote=L01,type=IMTOREG&REM,reg=NONE,data=INIT_COMPARE,hr_data=INIT_HR_DELAY};

; Branch back to the beginning.

L03 BR { next= L00, cond_addr=L00, event= NOCOND }